## Slide 1: Shared Memory Multiprocessors
A. Jantsch, professor, KTH, Sweden
Z. Lu, professor, KTH, Sweden
I. Sander, professor, KTH, Sweden
Courtesy:

## Slide 2: Outline
2
Shared memory architectures
  Centralized memory
  Distributed memory
Caches
  Write through / write-back caches
  The cache coherency problem

## Slide 3: Shared Memory Architectures

## Slide 4: Shared Memory Architectures
Shared Memory Multiprocessor are often used
  Symmetric Multiprocessors (SMP)
    Symmetric access to all of main memory from any processor
    also called UMA (uniform memory access)
  Distributed Shared Memory (DSM)
    Access time depends on the location of data word in memory
    also called NUMA (non-uniform memory access)

## Slide 5: Shared Memory Architectures
A shared memory programming model has a direct representation in hardware
Caches
  Increase performance
  Demand cache coherence and memory consistency protocols

## Slide 6: Memory Bandwidth
Rate of data transfer to or from memory often measured in Gbytes/sec
Depends upon
  Clock speed of memory
  Number of data channels available
  Width of each data channel

## Slide 7: Shared Cache Architecture
Several processors are connected via a switch with a shared memory
Has been used for a very small number of processors
Is difficult to use for a large number of processors, since the shared cache must deliver an extremely large bandwidth
P1
Pm
Switch
Cache
Main Memory

## Slide 8: Bus-shared Memory
The interconnect is a shared bus between the processors local caches and the memory
Has been used up to 20 to 30 processors
Scaling is limited due to the bandwidth limitations of the shared bus
P1
Pm
Cache
Main Memory
Cache
Bus

## Slide 9: Dancehall Architecture
Scalable Point-to-Point Network placed between caches and memory modules that together form the main memory
Due to the size of the interconnection network, the memory can be very far from the processors
P
1
P
m
Memory
Cache Cache
Interconnection Network
Memory

## Slide 10: Distributed Memory
No symmetric approach
      The local memory is much closer than the rest of the global memory
Structure works very well with scaling
Important in the design to use the local memory efficiently
cc-NUMA
Locality aware task scheduling
P1
Pm
Cache
Memory
Cache
Interconnection Network
Memory

## Slide 11: ARM’s Cortex-A9
January 25, 2011 SoC Architecture 10
L2 Cache Controller (PL310)
Cache-2-Cache
Transfers
Snoop Filtering
Generalized Interrupt Control and Distribution
Snoop Control Unit (SCU)
Timers
Advanced Bus Interface Unit
Optional 2nd I/F with Address Filtering
Primary AMBA 3 64bit Interface
Accelerator Coherence
Port (AXI-3 Slave)
FPU/NEON
Cortex-A9 CPU
PTM
I/F
FPU/NEON
Cortex-A9 CPU
PTM
I/F
FPU/NEON
Cortex-A9 CPU
PTM
I/F
FPU/NEON
Cortex-A9 CPU
Instruction | Data | Instruction | Data | Instruction | Data | Instruction | Data
Cache | Cache | Cache | Cache | Cache | Cache | Cache | Cache
PTM
I/F
ACP AXI-3 Slave
ACP AXI-3 Master
ACP AXI-3 Master
H/W Accelerators 64-bit Non-cached AXI-3 Masters
Three AXI-buses on the Cortex-A9
  ACP port provides coherent access to L1 and L2 caches through the Snoop Control Unit
  Two AXI masters off of the L2 cache provide 8GB/s at 500Mhz access to the main SoC bus

## Slide 12: Tilera Gx Architecture
11
Source: https://www.pcmag.com/encyclopedia/term/tile-gx

## Slide 13: Cache Coherency

## Slide 14: Caches and Cache Coherence
Caches play key role in all cases
  Reduce average data access time
  Reduce bandwidth demands placed on shared interconnect
But private processor caches create a problem
  Copies of a variable can be present in multiple caches
  A write by one processor may not become visible to others
    They’ll keep accessing stale value in their caches
  Cache coherence problem
  Need to take actions to ensure visibility

## Slide 15: Cache Memories
A cache memory is used to reduce the access time to memory
Cache misses can occur since the cache is much smaller than the memory
Processor
Cache
Main Memory

## Slide 16: Cache Memories
The decision which parts of the memory reside in the cache is taken by a replacement-algorithm
There are different protocols for a write operation: Write-Back and Write-Through
Processor
Cache
Main Memory

## Slide 17: Cache Memories Read Operation
If the memory location is in the cache (cache hit), the data is read from the cache.
If the memory location is not in the cache (cache miss), the block containing the data (is read from memory) and the cache is updated.
Processor
Cache
Main Memory

## Slide 18: Cache Memories Write Operation (Write Hit)
Write-Through Protocol
  A write operation updates the main memory location
    depending on protocol cache may also be updated
Processor
Cache
Main Memory

## Slide 19: Cache Memories Write Operation (Write Hit)
Write-Back Protocol
  A write operation updates only the cache location and marks it as updated with an associated flag bit (dirty flag)
  The main memory is updated later, when the block containing the marked address is removed from the cache (Replacement Policy)
Processor
Cache
Main Memory

## Slide 20: Cache Memories Write Operation (Write Miss)
Since data is not necessarily needed on a write there are two options
  Write Allocate: The block is allocated on a write miss, followed by the corresponding write-hit actions
  No-Write Allocate: Write misses do not affect the cache, instead only the lower-level memory is updated
Processor
Cache
Main Memory

## Slide 21: Cache Memories Write Operation (Write Miss)
Write-through and write-back can be combined with
write-allocate or no-write-allocate
Typically
  Write-back caches use write-allocate
  Write-through uses no-write-allocate
Processor
Cache
Main Memory

## Slide 22: States for Cache Blocks
Write-through
  Invalid
  Valid
Write-Back
  Invalid
  Valid
  Dirty (not updated in memory)

## Slide 23: Cache Coherence Problem (Uniprocessor)
1
P P
2
Cache
Bus
Main Memory
P1 reads location u (value 5) from main memory
P3 reads location u from main memory
P3 writes u, changing the value to 7
P1 reads value u again
P2 reads location u from main memory
P
3
Single Processor running 3 processes
Write-Back Cache

## Slide 24: Cache Coherence Problem (Uniprocessor)
P1 reads location u (value 5) from main memory
  Cache of P1 is updated
  The block containing u=5 is loaded into the cache
1
P P
2
Main Memory
P
3
Single Processor running 3 processes
u=5
Cache
Bus
Read
u=5

## Slide 25: Cache Coherence Problem (Uniprocessor)
P3 reads location u from main memory
  Cache and Memory have still the value u=5
1
P P
2
Cache
Main Memory
Bus
P
3
Single Processor running 3 processes
u=5
u=5
Read

## Slide 26: Cache Coherence Problem (Uniprocessor)
P3 writes u, changing the value to 7
  Cache is updated (u=7) and u is marked (Dirty)
  Memory is not changed!
1
P P
2
Cache
Main Memory
Bus
P
3
Single Processor running 3 processes
u=5
u=7
Write

## Slide 27: Cache Coherence Problem (Uniprocessor)
P1 reads value u again
  Since cache is common to all processes, there is no problem though the main memory is not updated! All processes have the same view of the cache!
Cache
Main Memory
Bus
3
Single Processor running 3 processes
u=5
P1 P2 P
Read
u=7

## Slide 28: Cache Coherence Problem (Uniprocessor)
P2 reads location u from main memory
  Since cache is common to all processes, there is no problem though the main memory is not updated! All processes have the same view of the cache!
1
P P
2
Main Memory
Bus
P
3
Single Processor running 3 processes
u=5
Read
Cache
u=7

## Slide 29: Cache Coherence Problem (Uniprocessor)
If only a uniprocessor is involved there is no cache coherence problem!
However, if another device on the bus is involved that has direct memory access (like a DMA), the cache may not represent the contents of the memory and the cache coherence problem can occur!

## Slide 30: Cache Coherence Problem
Cache
Cache
Bus
Main Memory
P1 reads location u (value 5) from main memory
P3 reads location u from main memory
P3 writes u, changing the value to 7
P1 reads value u again
P2 reads location u from main memory
P1 P2 P3
Cache

## Slide 31: Cache Coherence Problem (Write-Through Cache)
P1 reads location u (value 5) from main memory
  P1’s cache is updated (u=5)
Cache
Main Memory
Cache
P1 P2 P3
Cache
u=5
Bus
Read
u=5

## Slide 32: Cache Coherence Problem (Write-Through Cache)
P3 reads location u from main memory
  P3’s cache is updated (u=5)
Cache
Main Memory
Cache
P1 P2 P3
Cache
u=5
u=5
Bus
Read
u=5

## Slide 33: Cache Coherence Problem (Write-Through Cache)
P3 writes u, changing the value to 7
  main memory is updated (u=7)
  P3’s cache is not up-dated (no-write-allocate), but block is invalidated
Cache
Main Memory
Bus
P1 P2 P3
u=7
u=5 (Inv)
Cache Cache
Write Through
u=5

## Slide 34: Cache Coherence Problem (Write-Through Cache)
P1 reads value u again
  P1 reads the value from the cache (u=5), which is not the correct value!
Cache
Main Memory
Cache
Bus
Cache
u=5 (Inv)
u=7
u=5
P1 P2 P3
Read

## Slide 35: Cache Coherence Problem (Write-Through Cache)
P2 reads location u from main memory
  P2 reads the value from the main memory (u=7)
Main Memory
Cache Cache Cache
Bus
u=5 (Inv)
u=7
u=5
P1 P2 P3
Read

## Slide 36: Cache Coherence Problem (Write-Back Cache)
P1 reads location u (value 5) from main memory
  P1’s cache is updated (u=5)
Cache
Main Memory
Cache
Bus
P1 P2 P3
Cache
u=5
u=5

## Slide 37: Cache Coherence Problem (Write-Back Cache)
P3 reads location u from main memory
  P3’s cache is updated (u=5)
Cache
Main Memory
Cache
P1 P2 P3
Cache
u=5
u=5
Bus
Read
u=5

## Slide 38: Cache Coherence Problem (Write-Back Cache)
P3 writes u, changing the value to 7
  P3’s cache is updated (u=7) and location u is marked
  Main memory is NOT updated!
Cache
Main Memory
Cache
Bus
Cache
u=5
P1 P2 P3
Write Back
u=7
u=5

## Slide 39: Cache Coherence Problem (Write-Back Cache)
P1 reads value u again
  P1 reads the value from the cache (u=5), which is not the correct value!
Cache
Main Memory
Cache
Bus
Cache
u=7
u=5
u=5
P1 P2 P3
Read

## Slide 40: Cache Coherence Problem (Write-Back Cache)
P2 reads location u from main memory
  P2 reads the value from the cache (u=5), which is not the correct value!
Cache
Main Memory
Bus
P1 P2 P3
Cache
u=7
u=5
u=5
Read
Cache

## Slide 41: Cache Coherence
Since communication between processors is done by means of shared memory, cache coherence must be guaranteed.
The hardware should support cache coherence!
Everybody should have the same view of the memory system!

## Slide 42: Next Lecture
Coherence Protocols