## Slide 1: Cache Coherence Protocols
A. Jantsch, professor, KTH, Sweden
Z. Lu, professor, KTH, Sweden
I. Sander, professor, KTH, Sweden
Courtesy:

## Slide 2: Formal Definition of Coherence
Results of a program: values returned by its read operations
A memory system is coherent if the results of any execution of a program are such that it is possible to construct a hypothetical serial order of all operations that is consistent with the results of the execution and in which:
  Operations issued by any particular process occur in the order issued by that process, and
  The value returned by a read is the value written by the last write to that location in the serial order

## Slide 3: Formal Definition of Coherence
Two necessary features:
  Write propagation: value written must become visible to others
  Write serialization: writes to a location seen in same order by all
    if I see w1 before w2, you should not see w2 before w1
    no need for analogous read serialization since reads not visible to others

## Slide 4: Example
Task A
x:=0;
y:=0;
Print (x+y);
Task B
x:=1; y:=x+2;
x:=1; y:=x+2;
x:=0;
y:=0;
Print (x+y);
0
x:=0;
y:=0;
x:=1; y:=x+2;
Print (x+y);
4
x:=0;
x:=1; y:=x+2;
y:=0;
Print (x+y);
1
x:=1;
x:=0;
y:=0;
y:=x+2;
Print (x+y);
2
Coherent memory system

## Slide 5: Example
Task A
x:=0;
y:=0;
Print (x+y);
Task B
x:=1; y:=x+2;
x:=0;
y:=0;
x:=1;
y:=x+2;
y3
Print (x+y); x1
3
Incoherent memory system

## Slide 6: Snooping-based Cache Coherence

## Slide 7: Cache Coherence Using a Bus
Built on
  Bus transactions
  State transition diagram in cache
Uniprocessor bus transaction:
  Serialization of bus transactions

## Slide 8: Cache Coherence Using a Bus
Uniprocessor cache states:
  Effectively, every block is a finite state machine
  Write-through, write no-allocate has two states: valid, invalid
  Write-back, write-allocate caches have one more state: modified (“dirty”)
Multiprocessors extend
  cache states and
  bus transactions
to implement coherence

## Slide 9: Snooping-based Coherence Basic Idea
Transactions on bus are visible to all processors
Processors or cache controllers can snoop (monitor) bus and take action on relevant events (e.g. change state)

## Slide 10: Snooping-based Coherence Implementing a Protocol
Cache controller now receives inputs from both sides:
  Requests from processor, bus requests/responses from snooper
In either case, takes zero or more actions
  Updates state, responds with data, generates new bus transactions
Protocol is distributed algorithm: cooperating state machines
  Set of states, state transition diagram, actions
Granularity of coherence is typically cache block
  Like that of allocation in cache and transfer to/from cache

## Slide 11: Cache Coherence with Write- Through Caches
Key extensions to uniprocessor: snooping, invalidating/updating caches
  no new states or bus transactions in this case
  invalidation- versus update-based protocols
Write propagation: even in invalidation case, later reads will see new value
  invalidation causes miss on later access, and memory up-to-date via write-through
Cache
Main Memory
Bus
P1 Pn
Cache
Cache-Memory Transition
Bus Snooping
V
I
V
I
Cache Coherence Protocol

## Slide 12: State Transition Diagram Write-Through Cache (Write no allocate)
I
V
PrRd/BusRd
PrWr/BusWr
PrRd/-
PrWr/BusWr
BusWr/-
Processor-initiated transactions Bus-snooper-initiated transactions
Protocol is executed for each cache-controller connected to a processor
Cache Controller receives inputs from processor and bus
Block is not in Cache Block is in Cache

## Slide 13: State transition diagram (valid- Invalid protocol) Write back cache

## Slide 14: Problem with Write-Through
High bandwidth requirements
  Every write from every processor goes to shared bus and memory
  Write-through especially unpopular for Symmetric Multi- Processors
Write-back caches absorb most writes as cache hits
  Write hits don’t go on bus
  But now how do we ensure write propagation and serialization?
  Need more sophisticated protocols: large design space

## Slide 15: Limitation of Valid / Invalid protocol
All processor write to a local block will generate BusWrite both in write through and write back caches
BusWrite protocol action is generated even if CMP is used to
  Improve performance of an explicitly parallel program
  Run multiple parallel applications
Processor reads to an invalid block will read from main memory
Modified state is included in MSI protocol
  Processor reads to an invalid block will be served by modified cache node (if block is in modified state at some node) and will not generate bus transaction
  Modified block is the only valid copy of the block in the system
  Processor reads and writes can be carried out in local block without need to generate any protocol action
  Used in commercial machines
  Shared block has multiple valid copies in the systems

## Slide 16: Basic MSI Writeback Invalidation Protocol
States
  Invalid (I)
  Shared (S): memory and one or more caches have a valid copy
  Dirty or Modified (M): only one cache has a modified (dirty) copy
Processor Events:
  PrRd (read)
  PrWr (write)
Bus Transactions
  BusRd: asks for copy with no intent to modify
  BusRdX: asks for an exclusive copy with intent to modify
  BusWB: updates memory on write back
Actions
  Update state, perform bus transaction, flush value onto bus

## Slide 17: MSI State Transition Diagram (Write back cache)

## Slide 18: Limitation of MSI protocol
If processor P1 reads memory block B1 in its cache it is in Shared state
Now if processor writes to this block Bus Upgrade protocol action is generated
This action is unnecessary since this block is only read by P1 and other processors do not have it by now
Solution
  Add Exclusive state meaning that this is the only copy of the block in the system to the MSI protocol
Clean miss is served by memory and not by the cache
Both clean and dirty blocks must be served by cache
Solution
  Addition of Ownership state to the MSI protocol

## Slide 19: MOESI protocol
M
S
I
O
E
PrWr/-
PrRd/-
BusRd/Flush
BusRdX/Flush
PrWr/BusUpgd
PrWr/-
PrWr/BusRdx
PrWr/BusUpgd
BusRd/- BusRdX/- BusUpgd/-
PrRd/BusRd
S=0
PrRd/BusRd
S=1
BusRdx/Flush
BusRdX/-
BusUpgd/-
BusRdx/Flush
BusUpgd/-
PrRd/-
BusRd/Flush
PrRd/-
PrRd/-
BusRd/Flush

## Slide 20: Modern Bus Standards and Cache Coherence Protocols
Both the AMBA and the Avalon protocols do not include a cache coherence protocol!
The designer has to be aware of problems related to cache coherence
We see cache coherence protocols for SoCs coming
  E.g. ARM11 MPCore Platform support data cache coherence

## Slide 21: ARM11 MPCore Cache
Write back
Write allocate
MESI Protocol
  Modified: Exclusive and modified
  Exclusive: Exclusive but not modified
  Shared
  Invalid
Source: https://www.arm.com/products/silicon-ip-cpu

## Slide 22: Directory Based Cache Coherence

## Slide 23: Networks on Chip
In Networks-on-Chip cache coherence cannot be implemented by bus snooping!
P
MEM
Switch
Channel
NI
NI
NI
NI
Network Interface
C
P
MEM
C
P
MEM
C
P
MEM
C

## Slide 24: Distributed Memory
Distributed Memory Architectures which do not have a bus as only communication channel cannot use snooping protocols to ensure cache coherence
Instead a directory based approach can be used to guarantee cache coherence
P
1
P
m
Cache
Memory
Cache
Interconnection Network
Memory

## Slide 25: Directory-Based Cache Coherence Concepts
State of caches is maintained in a directory
A cache miss results in a communication between the node where the cache miss occures and the directory
Then information in affected caches is updated
Each node monitors the state of its cache with e.g. an MSI protocol

## Slide 26: Multiprocessor with Directories
Directory
Memory
Communication Assist
Cache
P
CA
C
Interconnection Network
Every block of main memory (the size of a cache block) has a directory entry that keeps track of its cached copies and the state
Directory
Memory
P
CA
C

## Slide 27: Tasks of the Protocol
When a cache miss occurs the following tasks have to be performed
  Finding out information of the state of copies in other caches
  Location of these copies, if needed (e.g. for Invalidation)
  Communication with other copies (e.g. obtaining data)

## Slide 28: Some Definitions
Home Node: Node with the main memory where the block is located
Dirty Node: Node, which has a copy of the block in modified (dirty) state
Owner Node: Node, that has a valid copy of the block and thus must supply data when needed (is either home or dirty node)
Exclusive Node: Node, that has a copy of the block in exclusive state (either dirty or clean)
Local Node (Requesting Node): Node, that has the processor issuing a request for the cache block
Locally Allocated Blocks: Blocks whose home is local to the issuing processor
Remotely Allocated Blocks: Blocks whose home is not local to the issuing processor

## Slide 29: Read Miss to a Block in modified State in Cache
C
P
CA
Memory/Dir
Requestor
C
P
CA
Memory/Dir
Directory Node for block
C
P
Memory/Dir
CA
Node with dirty copy
Read request to directory
1
Response with owner identity
2
Read request to owner
3
4a
Data Reply
4b
Revision message
to directory (Data Reply)

## Slide 30: Write Miss to a Block with Two Sharers
C
P
CA
Memory/Dir
Requestor
C
P
CA
Memory/Dir
Directory Node for block
C
P
CA
Memory/Dir
Node with shared copy
ReadEx request to directory
1
Response with Sharer’s identity
2
C
P
CA
Memory/Dir
Node with shared copy
4b
Invalidation Acknowledgement
Invalidation request to sharer
3a
Invalidation request to sharer
3b
Invalidation
Acknowledgement
4a

## Slide 31: Organization of the Directory
A natural organization of the directory is to maintain the directory information for a block together with the block in main memory
Each block can be represented as a bit vector of p presence bits and one or more state bits.
In the simplest case there is one state bit (dirty bit), which represents if there is a modified (dirty) copy of the cache in one node

## Slide 32: Example for Directory Information
x
x
Dirty Bit
Presence Bits
An entry for a memory block consists of presence bits and a status bit (dirty bit)
If dirty == ON, there can only be one presence bit set
P
CA
C
Memory
Directory

## Slide 33: Read Miss of Processor i
If the dirty == OFF
  Assist obtains the block from main memory, supplies it to the requestor and sets the presence bit p[i] ← ON
If the dirty == ON
  Assist responds to the requestor with the identity of the owner node
  Requester then sends a request network transaction to owner node
  Owner changes its state to shared and supplies the block to both the requesting node and the main memory
  The memory sets dirty ← OFF and p[i] ← ON

## Slide 34: Write Miss of Processor i
If the dirty == OFF
  The main memory has a clean copy of data
  The home node sends the presence vector to the requesting node i together with the data
  The home node clears its directory entry, leaving only the p[i] ← ON and dirty ← ON
  The assist at the requestor sends invalidation requests to the nodes where the value of the presence bit was ON and waits for an acknowledgement
  The requestor places the block in its cache in dirty state (dirty ← ON)

## Slide 35: Write Miss of Processor i
If the dirty == ON
  The main memory has not a clean copy of data
  The home node requests the cache block from the dirty node, which sets its cache state to invalid
  Then the block is supplied to the requesting node, which places the block in cache in dirty state
  The home node clears its directory entry, leaving only the p[i] ← ON and dirty ← ON

## Slide 36: Size of Directory 1 entry/memory block
SD = ST/SB x (N+1)
SD …size of directory ST … total memory
N … no of nodes CB…blocks per cache SB … block size
SC … cache size
Example:
ST = 4GB
N= 64 nodes CB = 128 K
SB = 64 Byte SC = 8 MB SD = 520MB
13% of total memory 102% of total cache size

## Slide 37: Size of Directory 1 entry/cache block
SD = N x CB x (N+1)
SD …size of directory ST … total memory
N … no of nodes CB…blocks per cache SB … block size
SC … cache size
Example:
ST = 4GB
N= 64 nodes CB = 128 K
SB = 64 Byte SC = 8 MB SD = 65 MB
1.5% of total memory 12.6% of total cache size

## Slide 38: Discussion
Directory based protocols allow to provide cache coherence for distributed shared memory systems, which are not based on buses
Since the protocol requires communication between nodes with shared copies there is a potential for congestion
Since communication is not instantly and varies from node to node there is the risk that there are different views of the memory at some time instances. These race conditions have to be understood and taken care of!