## Slide 1: Memory Hierarchies
Courtesy: Prof. Mats Brorsson, KTH, Sweden

## Slide 2: Contents
Memory
  DRAM
Caches
Memory Management

## Slide 3: Core Memory
Core memory was first large scale reliable main memory
  Invented by Forrester in late 40s/early 50s at MIT for Whirlwind project
Bits stored as magnetization polarity on small ferrite cores threaded onto two-dimensional grid of wires
Coincident current pulses on X and Y wires would write cell and also sense original state (destructive reads)
Core memory: DEC PDP-8/E Board,
4K words x 12 bits, (1968)
Robust, non-volatile storage
Used on space shuttle computers until recently
Cores threaded onto wires by hand (25 billion a year at peak production)
Core access time ~ 1ms
Notes: Early machines had things like mercury delay lines (jse)
Photo from David Gesswein djg@pdp8.net

## Slide 4: State of the art SSD
Samsung 990 PRO
Capacity 4TB
Sequential read
  4TB: Up to 7,450 MB/s
Sequential write
  4TB: Up to 6,900 MB/s
Source: https://semiconductor.samsung.com/consumer-storage/internal-ssd/990-pro/

## Slide 5: DRAM (Laptops/Desktops/Servers)
DIMM (Dual Inline Memory Module) contains multiple chips with clock/control/address signals connected in parallel (sometimes need buffers to drive signals to all chips)
Data pins work together to return wide word (e.g., 64-bit data bus using 16x4-bit parts)
Address lines multiplexed row/column address
Clock and control signals
Data bus
(4b,8b,16b,32b)
DRAM chip
~12
~7

## Slide 6: DRAM Architecture
Row Address Decoder
Col.
1
Col. 2M
Row 1
Row 2N
Column Decoder & Sense Amplifiers
M
N
N+M
bit lines
word lines
Memory cell (one bit)
D
Data
Bits stored in 2-dimensional arrays on chip
Modern chips have around 4-8 logical banks on each chip
  each logical bank physically implemented as many smaller arrays

## Slide 7: DRAM Operation
Three steps in read/write access to a given bank
Row access (RAS)
  Decode row address, enable addressed row (often multiple Kbytes in a row)
  Bit-lines share charge with storage cell
  Small change in voltage detected by sense amplifiers which latch whole row of bits
  Sense amplifiers drive bit-lines full rail to recharge storage cells
Column access (CAS)
  Decode column address to select small number of sense amplifier latches (4, 8, 16, or 32 bits depending on DRAM package)
  On read, send latched bits out to chip pins
  On write, charge sense amplifier latches which then charge storage cells to required value
  Can perform multiple column accesses on same row without another row access (burst mode)
Pre-charge
  Charges bit lines to known value, required before next row access
Each step has a latency of around 15-20ns in modern DRAMs
Various DRAM standards (DDR, RDRAM) have different ways of encoding the signals for transmission to the DRAM, but all share same core architecture
Notes: Use RAS/CAS to reduce average latency.

## Slide 8: Double-Data Rate (DDR2) DRAM
[ Micron, 256Mb DDR2 SDRAM datasheet ]
Row
Column
Precharge
Row’
Data
200MHz Clock
400Mb/s Data Rate

## Slide 9: Addressing the Processor-Memory Performance GAP
Goal: Illusion of large, fast, cheap memory
  Let programs address a memory space that scales to the disk size, at a speed that is usually as fast as register access
Solution: Put smaller, faster “cache” memories between CPU and DRAM
  Create a “memory hierarchy”

## Slide 10: Levels of the Memory Hierarchy
CPU Registers
100s Bytes
<10s ns
Cache
K Bytes
10-100 ns
1-0.1 cents/bit
Main Memory
M Bytes
200ns- 500ns
$.0001-.00001 cents /bit
Disk
G Bytes, 10 ms (10,000,000 ns)
10 - 10 cents/bit
-5
-6
Capacity
Access Time
Cost
Tape
infinite
sec-min
10
-8
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger
Today’s
Focus

## Slide 11: Typical Memory Hierarchy

## Slide 12: CPU-Memory Bottleneck
Memory
CPU
Performance of high-speed computers is usually
limited by memory bandwidth & latency
  Latency (time for a single access)
    Memory access time >> Processor cycle time
  Bandwidth (number of accesses per unit time)
    Number of data channels
    Clock speed of memory
    Width of one channel

## Slide 13: Physical Size Affects Latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations

## Slide 14: Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  if data Ï fast memory  long latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 15: In summary
Dynamic RAM (DRAM) is main form of main memory storage in use today
  Holds values on small capacitors, need refreshing (hence dynamic)
  Slow multi-step access: pre-charge, read row, read column
Static RAM (SRAM) is faster but more expensive
  Used to build on-chip memory for caches
Cache holds small set of values in fast memory (SRAM) close to processor
  Need to develop search scheme to find values in cache, and replacement policy to make space for newly accessed locations
Caches exploit two forms of predictability in memory reference streams
  Temporal locality, same location likely to be accessed again soon
  Spatial locality, neighboring location likely to be accessed soon

## Slide 16: Contents
Memory
  DRAM
Caches
Memory Management

## Slide 17: Common Predictable Patterns
Two predictable properties of memory references:
Temporal Locality: If a location is referenced, it is likely to be referenced again soon
Spatial Locality: If a location is referenced it is likely that locations near it will be referenced soon (e.g., array access)
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 18: Memory Reference Patterns
Source: Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality
Bad locality behavior

## Slide 19
Caches
Caches exploit both types of predictability:
  Exploit temporal locality by remembering the contents of recently accessed locations
  Exploit spatial locality by fetching blocks of data around recently accessed locations

## Slide 20: Cache Algorithm (Read)
HIT - Found in Cache
Return copy
of data from
cache
MISS - Not in cache
Read block of data from Main Memory
Wait …
Return data to processor
and update cache
Look at Processor Address, search cache tags to find match then either,
Hit Rate = fraction of accesses found in cache
Miss Rate = 1 – Hit rate
Hit Time = Cache access time +
time to determine HIT/MISS
Miss Time = time to replace block in cache +
time to deliver block to processor
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 21
Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416

## Slide 22: 4 Questions for Memory Hierarchy
Q1: Where can a block be placed in the cache?
(Block placement)
Q2: How is a block found if it is in the cache? (Block identification)
Q3: Which block should be replaced on a miss? (Block replacement)
Q4: What happens on a write? (Write strategy)

## Slide 23: Q1: Where can a block be placed?
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Fully (2-way) Set Direct
Associative Associative Mapped
anywhere anywhere in only into
set 0 block 4
(12 mod 4) (12 mod 8)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
Block 12
can be placed
0
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?

## Slide 24: Q2: How is a block found?
Index selects which set to look in
Tag on each block
  No need to check index or block offset
Increasing associativity shrinks index, expands tag. Fully Associative caches have no index field.
Block
Offset
Block Address
Index
Tag
Memory Address

## Slide 25: Direct-Mapped Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 26: 2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t

## Slide 27: Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t

## Slide 28: What causes a MISS?
Three Major Categories of Cache Misses:
  Compulsory Misses: first access to a block
  Capacity Misses: cache cannot contain all blocks needed to execute the program
  Conflict Misses: block replaced by another block and then later retrieved - (affects set assoc. or direct mapped caches)
    Nightmare Scenario: ping pong effect!

## Slide 29: Block Size and Spatial Locality
Word3
Word0
Word1
Word2
Larger block size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing block size?
block address offsetb
2b = block size a.k.a line size (in bytes)
Split CPU address
b bits
32-b bits
Tag
Block is unit of transfer between the cache and memory
4 words block, b=2
Fewer blocks => more conflicts. Can waste bandwidth.
Notes: Larger block size will reduce compulsory misses (first miss to a block).
Larger blocks may increase conflict misses since the number of blocks
is smaller.

## Slide 30: Q3: Which block should be replaced on a miss?
Easy for Direct Mapped
Set Associative or Fully Associative:
  Random
  Least Recently Used (LRU)
    LRU cache state must be updated on every access
    true implementation only feasible for small sets (2-way)
    pseudo-LRU binary tree often used for 4-8 way
  First In, First Out (FIFO) a.k.a. Round-Robin
    used in highly associative caches

## Slide 31: Write Through and Write Back Topologies

## Slide 32: Q4: What happens on a write?
Cache hit:
  write through: write both cache & memory
    Generally, higher traffic for main memory, but simplifies cache coherence
    A store buffer can retire store without exposing the processor to the access latency of lower-level cache
  write back: write cache only (Memory is written only when the entry is evicted)
    A dirty bit per block can further reduce the traffic
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 33: Write Policy Choices
Cache hit:
  write through: write both cache & memory
    Generally higher traffic but simpler pipeline & cache design
  write back: write cache only, memory is written only when the entry is evicted
    A dirty bit per block further reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 34: 5 Basic Cache Optimizations
Reducing Miss Rate
  Larger Block size (compulsory misses are reduced but conflict misses are increased)
  Larger Cache size (reduces capacity and conflict misses but increases hit time)
  Higher Associativity (conflict misses are reduced but requires more comparators)
Reducing Miss Penalty
  Multilevel Caches with inclusion
    But can reduce available cache size for processor
Reducing hit time
  Giving Reads Priority over the Writes
  E.g., Read complete before earlier writes in write buffer

## Slide 35: CPU-Cache Interaction (5-stage pipeline)
PC
addr
inst
Primary
Instruction
Cache
0x4
Add
IR
D
nop
hit?
  PCen
Decode,
Register
Fetch
wdata
R
addr
wdata
rdata
Primary
Data
Cache
we
A
B
Y
Y
ALU
MD1
MD2
Cache Refill Data from Lower Levels of Memory Hierarchy
hit?
Stall entire CPU on data cache miss
To Memory Control
M
E
Notes: How are writes to istream handled?

## Slide 36: Improving Cache Performance
Average memory access time =
Hit time + Miss rate x Miss penalty
Example: 1 cycle (hit time)+(0.05)x(30)=2.5cycles!!
To improve performance:
  reduce the hit time
  reduce the miss rate
  reduce the miss penalty
Hit time and miss rate are conflicting
What is the simplest design strategy?
Biggest cache that doesn’t increase hit time past 1-2 cycles (approx 8-32KB in modern technology)
[ design issues more complex with out-of-order superscalar processors ]
Notes: Design the largest primary cache without slowing down the clock
Or adding pipeline stages.

## Slide 37: Serial-versus-Parallel Cache and Memory access
a is HIT RATIO: Fraction of references in cache
1 - a is MISS RATIO: Remaining references
CACHE
Processor
Main
Memory
Addr
Addr
Data
Data
Average access time for serial search: tcache + (1 - a) tmem
CACHE
Processor
Main
Memory
Addr
Data
Data
Average access time for parallel search: a tcache + (1 - a) tmem
Savings are usually small, tmem >> tcache, hit ratio a high
High bandwidth required for memory path
Complexity of handling parallel paths can slow tcache

## Slide 38: Causes for Cache Misses
Compulsory: first-reference to a block a.k.a. cold start misses
- misses that would occur even with infinite cache
Capacity: cache is too small to hold all data needed by the program
- misses that would occur even under perfect
replacement policy
Conflict: misses that occur because of collisions
due to block-placement strategy
    - misses that would not occur with full associativity

## Slide 39: Effect of Cache Parameters on Performance (Review)
Larger cache size
  reduces capacity and conflict misses
  hit time will increase
Higher associativity
  reduces conflict misses
  may increase hit time
Larger block size
  reduces compulsory and capacity (reload) misses
  increases conflict misses and miss penalty
Notes: Requested block first….
The following could be in the slide…
spatial locality reduces compulsory misses and capacity reload misses
  fewer blocks may increase conflict miss rate
  larger blocks may increase miss penalty

## Slide 40: Write Performance
Tag
Data
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
WE
Notes: Completely serial (jse)

## Slide 41: Reducing Write Hit Time
Problem: Writes take two cycles in memory stage, one cycle for tag check plus one cycle for data write if hit
Solutions:
Fully-associative (CAM Tag) caches: Word line only enabled if hit
Pipelined writes: Hold write data for store in single buffer ahead of cache, write cache data during next store’s tag check
Notes: Need to bypass from write buffer if read address matches write buffer tag!

## Slide 42: Pipelining Cache Writes
Tags
Data
Tag
Index
Store Data
Address and Store Data From CPU
Delayed Write Data
Delayed Write Addr.
=?
=?
Load Data to CPU
Load/Store
L
S
1
0
Hit?
Data from a store hit written into data portion of cache during tag access of subsequent store

## Slide 43: Write Buffer to Reduce Read Miss Penalty
Processor is not stalled on writes, and read misses can go ahead of write to main memory
Problem: Write buffer may hold updated value of location needed by a read miss
Simple scheme: on a read miss, wait for the write buffer to go empty
Faster scheme: Check write buffer addresses against read miss addresses, if no match, allow read miss to go ahead of writes, else, return value in write buffer
Data Cache L1
Unified L2 Cache
Reg File
CPU
Write
buffer
Evicted dirty lines for write back cache
OR
All writes in write through cache
Notes: Deisgners of the MIPS M/1000 estimated that waiting for a four-word buffer to empty
increased the read miss penalty by a factor of 1.5.

## Slide 44: Presence of L2 influences L1 design
Use smaller L1 if there is also L2
  Trade increased L1 miss rate for reduced L1 hit time and reduced L1 miss penalty
  Reduces average access energy
Use simpler write-through L1 with on-chip L2
  Write-back L2 cache absorbs write traffic, doesn’t go off-chip
  At most one L1 miss request per L1 access (no dirty victim write back) simplifies pipeline control
  Simplifies coherence issues
  Simplifies error recovery in L1 (can use just parity bits in L1 and reload from L2 when parity error detected on L1 read)

## Slide 45: Inclusion Policy
Inclusive multilevel cache:
  Inner cache holds copies of data in outer cache
  If a block is brought at inner level cache it must be allocated at outer level cache as well
  If a block is invalidated at inner level cache it must be removed at outer level cache as well
  External coherence snoop access need only check outer cache
Exclusive multilevel caches:
  Inner cache may hold data not in outer cache
  Swap lines between inner/outer caches on miss
  Victim is written in L2
  Used in AMD Athlon with 64KB primary and 256KB secondary cache
Why choose one type or the other?
Notes: New slide (jse)

## Slide 46: Reduce miss penalty of long blocks
Do not wait for full block before restarting the CPU
  Early restart
  Critical word first

## Slide 47: Non-blocking Caches
Blocking cache
  one processor access at a time
  Suitable for 5 stage pipeline
  Not suitable for a machine that can execute multiple memory accesses in one cycle
Increase cache bandwidth with non blocking caches
Overlapping cache accesses
Non-blocking caches are used in
  Modern wide-issue Out of Order processors because
  Memory access throughput must be sustained
  Memory accesses must execute concurrently
    To hide the large penalty of cache misses

## Slide 48: Non-blocking caches
A miss in cache is allocated in
  Miss Status Handling Register (MSHR)
MSHR has information
  Cache line allocated to miss
  Block address
  Destination register of load
Overlapped miss requests to same block are allowed
  Primary miss
  Secondary miss
Intel Pentium Pro supports four outstanding memory misses

## Slide 49: Itanium-2 On-Chip Caches (Intel/HP, 2002)
Level 1: 16KB, 4-way s.a., 64B line, quad-port (2 load+2 store), single cycle latency
Level 2: 256KB, 4-way s.a, 128B line, quad-port (4 load or 4 store), five cycle latency
Level 3: 3MB, 12-way s.a., 128B line, single 32B port, twelve cycle latency
Notes: If two is good, then three must be better (jse)

## Slide 50: Power 7 On-Chip Caches [IBM 2009]
32KB L1 I$/core
32KB L1 D$/core
3-cycle latency
256KB Unified L2$/core
8-cycle latency
32MB Unified Shared L3$
Embedded DRAM
25-cycle latency to local slice

## Slide 51: Prefetching
Speculate on future instruction and data accesses and fetch them into cache(s)
  Instruction accesses easier to predict than data accesses
Varieties of prefetching
  Hardware prefetching
  Software prefetching
  Mixed schemes
What types of misses does prefetching affect?
Notes: Reduces compulsory misses, can increase conflict and
capacity misses.

## Slide 52: Issues in Prefetching
Usefulness – should produce hits
Timeliness – not late and not too early
Cache and bandwidth pollution
L1 Data
L1 Instruction
Unified L2 Cache
RF
CPU
Prefetched data

## Slide 53: Hardware Instruction Prefetching
Instruction prefetch in Alpha AXP 21064
  Fetch two blocks on a miss; the requested block (i) and the next consecutive block (i+1)
  Requested block placed in cache, and next block in instruction stream buffer
  If miss in cache but hit in stream buffer, move stream buffer block into cache and prefetch next block (i+2)
L1 Instruction
Unified L2 Cache
RF
CPU
Stream
Buffer
Prefetched
instruction block
Req
block
Req
block
Notes: Need to check the stream buffer if the requested block is in there.
Never more than one 32-byte block in the stream buffer.

## Slide 54: Hardware Data Prefetching
Prefetch-on-miss:
  Prefetch b + 1 upon miss on b
One Block Lookahead (OBL) scheme
  Initiate prefetch for block b + 1 when block b is accessed
  Why is this different from doubling block size?
  Can extend to N-block look-ahead
Strided prefetch
  If observe sequence of accesses to block b, b+N, b+2N, then prefetch b+3N etc.
Example: IBM Power 5 [2003] supports eight independent streams of strided prefetch per processor, prefetching 12 lines ahead of current access
Notes: HP PA 7200 uses OBL prefetching
Tag prefetching is twice as effective as prefetch-on-miss in
reducing miss rates.

## Slide 55: Software Prefetching
  for(i=0; i < N; i++) { prefetch( &a[i + 1] ); prefetch( &b[i + 1] ); SUM = SUM + a[i] * b[i]; }
Notes: Cache should be non-blocking or lockup-free.
By that we mean that the processor can proceed while the prefetched
Data is being fetched; and the caches continue to supply instructions
And data while waiting for the prefetched data to return.

## Slide 56: Software Prefetching Issues
Timing is the biggest issue, not predictability
  If you prefetch very close to when the data is required, you might be too late
  Prefetch too early, cause pollution
  Estimate how long it will take for the data to come into L1, so we can set P appropriately
  Why is this hard to do?
  for(i=0; i < N; i++) { prefetch( &a[i + P] ); prefetch( &b[i + P] ); SUM = SUM + a[i] * b[i]; }
Must consider cost of prefetch instructions

## Slide 57: Contents
Memory
  DRAM
Caches
Memory Management

## Slide 58
Memory Management

## Slide 59: Bare Machine

## Slide 60: Base and Bound Scheme

## Slide 61: Base and Bound Scheme

## Slide 62: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is the address translation on each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 63: Page tables encode virtual address spaces
A machine usually supports
pages of a few sizes
(MIPS R4000):
A valid page table entry codes physical memory “frame” address for the page
A virtual address space
is divided into blocks
of memory called pages
Physical
Address Space
Virtual
Address Space
frame
frame
frame
frame

## Slide 64: Page tables encode virtual address spaces
A machine usually supports
pages of a few sizes
(MIPS R4000):
Physical
Memory Space
A valid page table entry codes physical memory “frame” address for the page
A virtual address space
is divided into blocks
of memory called pages
frame
frame
frame
frame
A page table is indexed by a
virtual address
virtual address
Page Table
OS manages the page table for each process

## Slide 65: Details of Page Table
Physical
Memory Space
Page table maps virtual page numbers to physical frames (“PTE” = Page Table Entry)
Virtual memory => treat memory  cache for disk
Virtual Address
Page Table
index
into
page
table
Page Table
Base Reg
V
Access
Rights
PA
V page no.
offset
12
table located
in physical
memory
P page no.
offset
12
Physical Address
frame
frame
frame
frame
virtual address
Page Table

## Slide 66: VM and Disk: Page replacement policy
...
Page Table
1 0
used
dirty
1 0
0 1
1 1
0 0
Set of all pages
in Memory
Tail pointer:
Clear the used
bit in the
page table
Head pointer
Place pages on free list if used bit
is still clear.
Schedule pages with dirty bit set to
be written to disk.
Freelist
Free Pages
Dirty bit: page written.
Used bit: set to
1 on any reference
Architect’s role: support setting dirty and used bits

## Slide 67: Page tables may not fit in memory!
A table for 4KB pages for a 32-bit address space has 1M entries
Each process needs its own address space!
P1 index
P2 index
Page Offset
31
12
11
0
21
22
32-bit virtual address
Top-level table wired in main memory
Subset of 1024 second-level tables in main memory; rest are on disk or unallocated
Two-level Page Tables

## Slide 68: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 69: Inverted Page Table
Hierarchical page table
  Each process has its own set of page tables
  A lot of page table entries are still empty
Inverted page tables
  Inverted page table has one entry per physical page frame
    That it is shared by all processes
  Motivation
    There cannot be more valid page-table entries than there are page frames
  Size of page table
    Proportional to number of page frames
    Not to number of pages
  Shared by all processes
    Virtual page number is hashed to obtain one entry in inverted page table

## Slide 70: Inverted Page Table
Synonyms
  Solved since page table is shared
  All processes refer to same page with same VA
  Per process access rights
    Solved by memory segmentation
    Each VA points to a memory segment private to a process
    But segments are paged in a unique virtual space shared by all processes

## Slide 71: Translation Lookaside Buffer

## Slide 72: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in un-translated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 73: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Restart instruction
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 74: Page Fault Handler
When the referenced page is not in DRAM:
  The missing page is located (or created)
  It is brought in from disk, and page table is updated
    Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  If no free pages are left, a page is swapped out
    Pseudo-LRU replacement policy
Since it takes a long time to transfer a page (msecs), page faults are handled completely in software by the OS
  Untranslated addressing mode is essential to allow kernel to access page tables

## Slide 75: Handling VM-related exceptions
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Handling a page fault (e.g., page is on disk) needs a restartable exception so software handler can resume after retrieving page
  Precise exceptions are easy to restart
  Can be imprecise but restartable, but this complicates OS software
Handling protection violation may abort process
  But often handled the same as a page fault
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 76: Address Translation in CPU Pipeline
Need to cope with additional latency of TLB:
  slow down the clock?
  pipeline the TLB and cache access?
  virtual address caches
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 77: Virtual-Address Caches
one-step process in case of a hit (+)
cache needs to be flushed on a context switch unless address space identifiers (ASIDs) included in tags (-)
aliasing problems due to the sharing of pages (-)
maintaining cache coherence (-) (see later in course)
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
Alternative: place the cache before the TLB
CPU
VA
(StrongARM)
Virtual
Cache
PA
TLB
Primary
Memory

## Slide 78: Virtually Addressed Cache (Virtual Index/Virtual Tag)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Instruction / data
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Translate on miss

## Slide 79: Aliasing in Virtual-Address Caches
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data. Writes to one copy not visible to reads of other!
General Solution: Prevent aliases coexisting in cache
Software (i.e., OS) solution for direct-mapped cache
  VAs of shared pages must agree in cache index bits; this ensures all VAs accessing same PA will conflict in direct-mapped cache (early SPARCs)
Notes: Two processes sharing the same file,
Map the same memory segment to different
Parts of their address space.

## Slide 80: Concurrent Access to TLB & Large L1 The problem with L1 > Page size
Can VA1 and VA2 both map to PA ?
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Notes: If they differ in the lower ‘a’ bits alone, and share a physical page.

## Slide 81: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
  Cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 82: Virtual-Index Physical-Tag Caches: Associative Organization
How does this scheme scale to larger caches?
VPN a L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
2a
=
2a
After the PPN is known, 2a physical tags are compared
Notes:   Consider 4-Kbyte pages and caches with 32-byte blocks
  32-Kbyte cache  2a = 8
    4-Mbyte cache  2a =1024 No !

## Slide 83: A solution via Second Level Cache
Usually, a common L2 cache backs up both Instruction and Data L1 caches
L2 is “inclusive” of both Instruction and Data caches
  Inclusive means L2 has copy of any line in either L1
CPU
L1 Data Cache
L1 Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory

## Slide 84: Anti-Aliasing Using L2: MIPS R10000
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Direct-Mapped L2
PA a1 Data
PPN
into L2 tag
Suppose VA1 and VA2 both map to PA and VA1 is already in L1, L2 (VA1  VA2)
After VA2 is resolved to PA, a collision will be detected in L2.
VA1 will be purged from L1 and L2, and VA2 will be loaded  no aliasing !
Virtual index physical tag L1 & L2 caches

## Slide 85: Anti-Aliasing using L2 for a Virtually Addressed L1
VPN Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual
Index & Tag
Physical
Index & Tag
L1 VA Cache
L2 PA Cache
L2 “contains” L1
PA VA1 Data
VA1 Data
VA2 Data
“Virtual
Tag”
Physically-addressed L2 can also be used to avoid aliases in virtually-addressed L1

## Slide 86: Hashed Page Table: Approximating Associative Addressing
hash
Offset
Base of Table
+
PA of PTE
Primary
Memory
VPN PID PPN
Page Table
VPN d
Virtual Address
VPN PID DPN
VPN PID
PID
Hashed Page Table is typically 2 to 3 times larger than the number of PPN’s to reduce collision probability
It can also contain DPN’s for some non-resident pages (not common)
If a translation cannot be resolved in this table then the software consults a data structure that has an entry for every existing page (e.g., full page table)

## Slide 87: Power PC: Hashed Page Table
Base of Table
hash
Offset
+
PA of Slot
Primary
Memory
VPN PPN
Page Table
VPN d
80-bit VA
VPN
Each hash table slot has 8 PTE's <VPN,PPN> that are searched sequentially
If the first hash slot fails, an alternate hash function is used to look in another slot
All these steps are done in hardware!
Hashed Table is typically 2 to 3 times larger than the number of physical pages
The full backup Page Table is a software data structure

## Slide 88: VM features track historical uses:
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (not virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical

## Slide 89: Virtual Memory Use Today - 1
Servers/desktops/laptops/smartphones have full demand-paged virtual memory
  Portability between machines with different memory sizes
  Protection between multiple users or multiple tasks
  Share small physical memory among active tasks
  Simplifies implementation of some OS features
Vector supercomputers have translation and protection but rarely complete demand-paging
(Older Crays: base&bound, Japanese & Cray X1/X2: pages)
  Don’t waste expensive CPU time thrashing to disk (make jobs fit in memory)
  Mostly run in batch mode (run set of jobs that fits in memory)
  Difficult to implement restartable vector instructions

## Slide 90: Next Lecture
Chip multiprocessors