## Slide 1: Instruction Level Parallelism
Out of order dynamic processor

## Slide 2: Contents
Super-pipelined and super-scalar processors
Dynamically scheduled pipelines
Out of order execution
Tomasulo algorithm with speculation
Explicit register renaming and ROB

## Slide 3: Super Pipelined Architecture
When one of the stages in five stage pipeline takes more than one cycle and is further pipeline, we say that CPU is super-pipelined

## Slide 4: Superscalar Pipeline
CPUs can be superscalar meaning that more than one instruction is fetched decoded and issued in every cycle
Idea works well with workloads with both integer and floating point instructions
In case of superscalar, we use IPC=1/CPI, CPI is usually less than one
In practice, superscalar architectures may be super-pipelined as well

## Slide 5: Superscalar Pipeline
Fetch two instructions per cycle
  Issue both simultaneously if one is integer/memory and other is floating point
Same idea can be extended to wider issue by duplicating functional units
  E.g. 4-issue UltraSPARC & Alpha 21164 but regfile ports and bypassing costs grow quickly
Commit Point
2
PC
Inst. Mem
D
Dual
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Un-pipelined divider

## Slide 6: Strengths of Static Pipelines
Five stage pipeline is static because
  Five stage pipeline require compiler support to schedule the code to minimize the stalls in ID stage
Static pipelines are
  Power efficient
    Many activities done in dynamic processors are migrated to compiler
    Simple hardware
Because of predictable performance compiler can optimize code statically

## Slide 7: Weaknesses of Static Pipeline
Cache miss can not be handled efficiently
  Stall processor upon cache miss
Only one memory access at a time
  Can not address memory wall problem
Dynamic information such as memory addresses are not available at compile time
  Can not address data hazards on memory operands

## Slide 8: Weaknesses of Static Pipeline
Compiler of static pipeline becomes very complex
  Rely on microarchitectural features
    E.g., some static pipelines rely on compiler to insert NOOP between dependent instructions and avoid forwarding and stalling hardware. But such a code is not portable

## Slide 9: Weaknesses of Static Pipeline
Precise exceptions (Page fault in IF and ME stage, unimplemented instruction in ID) are hard to handle if instructions execute out of order

## Slide 10: Dynamically Scheduled Pipelines
In static pipelines an instruction only starts execution when
  Data, control and structural hazard free
Static pipelines can only reap ILP inside the basic block
Size of basic block is limited
  Five instructions usually
To increase the instruction level parallelism (ILP) instructions may execute in any order that respects the program dependencies
  Again because of data hazards more instructions are stalled and bypassed in ID stage

## Slide 11: Out of Order execution
To execute instructions in out of process order all data hazards on both register and memory operands along with control and structural hazards must be resolved
Solved by Tomasulo Algorithm

## Slide 12: Tomasulo Algorithm with Speculation

## Slide 13: Tomasulo Algorithm with Speculation
Instructions are fetched from I-cache in instruction fetch queue
Instructions wait in the issue queue until all their register operands are available
Results of instruction execution are dispatched on Common Data Bus (CDB)
The dispatch unit verifies all hazards on all register operands before sending instructions to the backend
Backend has issue queues
  An instruction holds an issue queue entry from dispatch till the end of its execution
  Instructions and their destination registers in issue queue are tagged with ID of issue queue entry
  Registers in register files are also tagged with the same ID

## Slide 14: Tomasulo Algorithm with Speculation
Dispatch logic
  Allocates an entry in issue queue designated by the instruction OP code
  Fetch input register values if available or tags if they are pending in the backend
  If tags are stored in input operands of an instruction it is marked as not ready
  If tags are not valid values are valid, then values are updated in input operand fields of instruction and marks it ready
  Result on CDB is both <value,tag>
    Updates instruction in issue queue with matching tags
    Updates register file with matching tags

## Slide 15: Tomasulo Algorithm with Speculation
Instruction can issue in next cycle
  When all input operands are available
  When functional unit is available
  When CDB is available after instruction completion
Load Store queue
  Keep process order of all issued loads and stores
  Solve hazards on out of order memory accesses
Address generation unit (AGU)
Both Load and Store are assigned entry in Load Store queue and in issue queue
Store is divided into two instructions
  SD-D bypass AGU
  SD-A calculates address
Load is tagged with tag of memory of the latest store
  Load can search for all store queue entries that are prior to it in process order but not yet completed

## Slide 16: Tomasulo Algorithm with Speculation
Data hazards are resolved in Load Store queue
  A ready Load can issue to memory queue if and only no pending store to same address is there in the Load Store queue
  A ready store can issue only if there is no pending load or store with same address is there in Load Store queue
  Addresses are not same most of the time
    But are unknown (not ready)
    Can be assumed to be same (conservative approach)

## Slide 17: Tomasulo with Speculation

## Slide 18: Tomasulo with Speculation
Branches
  Treated like integer instruction
  Tomasulo without speculation
    Dispatch unit stalls when it dispatches branch
    Till the outcome of the branch is available
    If untaken then dispatch unit continues to dispatch the instructions
    If taken, then instruction fetch queue is cleared
    Instructions are fetched from branch address now
Hazards on register operands is resolved by register renaming
  At any time, there may be multiple copies of same register may be pending in the backend
  The dispatch logic renames the register to the issue queue entry tag of the instruction that produces it

## Slide 19: Example
How all hazards on all register operands is resolved in the following code
  Load F0, 0(R1)
  ADD F1, F1, F0
  Load F0, 0(R2)
If first load misses in D-cache it goes to main memory
Second load hits in cache and completes long before first load
But ADD will read correct value of F0 by
  Looking for its tag on the CDB
  Value produced by the first load is never stored in register file

## Slide 20: Speculation (Branch prediction)
Branches act as fences and ILP can not be exploited beyond boundaries of basic blocks
  Solution is Branch prediction and branch target address speculation

## Slide 21: Branch Prediction
Motivation:
  Branch penalties limit performance of deeply pipelined processors
  Modern branch predictors have high accuracy
  (>95%) and can reduce branch penalties significantly
Required hardware support
  Prediction structures
    Branch history tables, branch target buffers, etc
  Misprediction recovery mechanisms
    Keep result computation separate from commit
    Kill instructions following branch in pipeline
    Restore state to the instruction following branch

## Slide 22: Dynamic Branch Prediction (Learning based on past behavior)
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 23: Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 24: Branch History Table
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 25: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 26: Branch Target Buffer
BP bits are stored with the predicted target address.
IF stage: If (BP=taken) then nPC=target else nPC=PC+4
later: check prediction, if wrong then kill the instruction
and update BTB & BPb else update BPb
IMEM
PC
Branch
Target
Buffer
(2k entries)
k
BPb
predicted
target
BP
target

## Slide 27: Tomasulo with Speculation

## Slide 28: Tomasulo with Speculation
Following needs to be supported in the architecture for speculative execution
  Recover from mis-predicted branches
  Branch prediction
  Branch target
  Temporary storage of uncommitted speculative results
  Support of precise exception
  Execute instructions speculatively and delay the results till instruction becomes non-speculative
  Execution is rolled back if branch was miss predicted or any prior instruction caused exception

## Slide 29: Reorder Buffer (ROB)
Is a managed FIFO
  Keeps track of dispatched instructions to
    Recover from mis-predicted branches and precise exceptions
    Temporary storage for registers which are targets of speculative instructions
Instructions are fetched in process order
Branches are predicted in BPB and BTB
Dispatch unit allocates entry in
  Issue queue and ROB entry, Load Store queue entry also for Load and Store instructions
Dispatch unit manages register renaming in Register Alias Table (RAT)
  An integer or floating point register can be
    Pending in the backend
    Speculative in ROB
    Committed in Register file

## Slide 30: ROB and RAT
RAT is accessed with architectural register number and returns
  Tag of the latest instruction modifying it
  Or register number of the register file
  Plus, one bit indicating if the value is pending in the backend
Dispatch unit renames the destination register with tag of the instruction in ROB
Same tag is stored for register in RAT and in register file
Input operands are looked up in RAT
  Value is available in Register file or ROB
  Tag of the instruction modifying it

## Slide 31: Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the
Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is de-allocated
Replacing the
tag by its value
is an expensive
operation

## Slide 32: Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 33: Renaming & Out-of-order Issue An example
When are tags in sources
replaced by data?
When can a name be reused?
1 LD F2, 34(R2)
2 LD F4, 45(R3)
3 MULTD F6, F4, F2
4 SUBD F8, F2, F2
5 DIVD F4, F2, F8
6 ADDD F10, F6, F4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
F1
F2
F3
F4
F5
F6
F7
F8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
v1
1 1 1 LD
0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 34: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-
Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 35: ROB
Instruction result is put on CDB as <tag,value> pair
  ROB, Issue queue, Reg file and RAT update the value
Speculative instruction retire at the top of the ROB in process order
Stores execute in the D-Cache when they reach at the top of the ROB
Branch outcome if different from prediction then
  Wait for branch to reach at top of the ROB
  Flush all instructions following branch
Precise exceptions are also taken when the faulting instruction reach at the top of the ROB
RAT is also made to point at that all values are in the register when in any case speculative execution is rolled back or exception is taken

## Slide 36: Dynamic Memory Disambiguation
Load Store queue keeps the process order of all memory operations and resolve all hazards on memory operands
Loads commit at the top of the ROB
  All previous stores and loads have already retired in process order
  No WAW and WAR hazards are possible
  RAW hazards are resolved by executing load if it is followed by a store by allowing store to complete first
  A completed store is one that has both address and data is ready
  If some prior store address is unknown then hardware assume that they are the same and load must wait for the store address to be available to check it
  It is rare that loads depend on prior stores in queue

## Slide 37: Dynamic Memory Disambiguation
If some prior store address is unknown then load can be issued speculatively assuming it is not equal
If later, when then address of store is known and is equal to the load then load and all subsequent instructions are replayed as if it was a mis-predicted branch
Loads are also predicted like branches

## Slide 38: Explicit Register Renaming
Register number from ISA
5
5
Front end RAT
Retirement RAT
Physical register file
7
7
Latest
Retired
Speculative

## Slide 39: Explicit Register Renaming
ROB keeps process order of the instructions and supports register renaming
Alternatively, ROB can only keep process order of the dispatched instructions and register renaming can be handled by register file
Physical register file is larger than registers accessed by the ISA (Architectural Registers)
For an architectural register physical register must hold its latest value (speculative or not) and its retired value committed value just in case exception occurs

## Slide 40: Explicit Register Renaming
Mapping from architectural to physical is done in two steps
Front End RAT
  Maps architectural registers to physical register holding its latest value plus one bit indicating if it is pending in the backend
Retirement RAT
  Maps architectural registers to physical register holding its latest committed value
In the dispatch stage
  New physical register is allocated to the instruction’s destination architectural register
  Front end RAT is looked up to fetch the latest value of the instruction’s input operands if it is not pending in the backend
  Otherwise, physical register number is send to issue queue and operands are marked not ready
  When a retired value is overwritten by another retired value of the same register then old physical register holding old retired value is reclaimed to the free list of physical registers

## Slide 41: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
ROB
Rename Table
Physical Regs
Free List
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<R1>
P8
p

## Slide 42: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8

## Slide 43: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 r3 P1

## Slide 44: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 r3 P1
P5
P3
x sub p P6 p P5 r6 P3

## Slide 45: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 r3 P1
P5
P3
x sub p P6 p P5 r6 P3
P1
P2
x add P1 P3 r3 P2

## Slide 46: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 r3 P1
P5
P3
x sub p P6 p P5 r6 P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4

## Slide 47: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 r1 P0
x add P0 r3 P1
x sub p P6 p P5 r6 P3
x ld p P7 r1 P0
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4
Execute & Commit
p
p
p
<R1>
P8
x

## Slide 48: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 r6 P3
x add P0 r3 P1
x add P0 r3 P1
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 r1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4
Execute & Commit
p
p
p
<R1>
P8
x
p
p
<R3>
P7

## Slide 49: Reorder Buffer Holds Active Instruction Window
…
ld r1, (r3)
add r3, r1, r2
sub r6, r7, r9
add r3, r3, r6
ld r6, (r1)
add r6, r6, r3
st r6, (r1)
ld r6, (r1)
…
(Older instructions)
(Newer instructions)
Cycle t
…
ld r1, (r3)
add r3, r1, r2
sub r6, r7, r9
add r3, r3, r6
ld r6, (r1)
add r6, r6, r3
st r6, (r1)
ld r6, (r1)
…
Commit
Fetch
Cycle t + 1
Execute

## Slide 50: Recovering ROB/Renaming Table
t
v
t
v
t
v
Register File
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available

## Slide 51: Next Session
Worked out examples